## Slide 1: Mali Instruction Set Architecture
Connor Abbott

## Slide 2: Background
Started 2 years ago at FOSDEM
Worked with Ben Brewer to reverse-engineer the ISA for Mali 200/400
Took ~6 months for reverse-engineering, 1.5 years for writing compilers and work still ongoing

## Slide 3: Mali Architecture
Mali 200/400: Midgard
  Geometry Processor (GP)
  Pixel Processor (PP)
Mali T6xx: Utgard
  Unified architecture

## Slide 4: Geometry Processor

## Slide 5: Architecture
Designed for multimedia as well (JPEG, H264, etc.)
Scalar VLIW architecture
Problem: how to reduce # of register accesses per instruction?
  Register ports are really expensive!

## Slide 6: Existing Solutions
Restrictions on input & output registers (R600)
Split datapath and register file in half (TI C6x)

## Slide 7: Feedback Registers
Idea: register ports are expensive, FIFO’s are cheap
Keep a queue of the last few results
Eliminate most register accesses

## Slide 8: Feedback Registers
ALU
ALU
Register File
mux
mux
FIFO
FIFO

## Slide 9: Compiler
Idea: programs on the GP look like a constrained dataflow graph
Instead of standard 3-address instructions (e.g. LLVM, TGSI) or expression trees (GLSL IR), our IR will consist of a directed acyclic graph of operations
The scheduler will place nodes in order to satisfy constraints

## Slide 10: Dataflow Graph
load r0
load r1
load r2
add
add
reciprocal
multiply
store r0

## Slide 11: Scheduled Dataflow Graph
 | Register Read | ALU 1 | ALU 2 | Output
Cycle 1 |  |  |  | 
Cycle 2 |  |  |  | 
Cycle 3 |  |  |  | 
Cycle 4 |  |  |  | 
load r0
load r1
load r2
add
add
rcp
mul
store r0

## Slide 12: Dependency Issues
add
store r0
multiply
load r0
store r1
?

## Slide 13: Dependency Issues
Solution: keep a list of side-effecting “root” nodes
Each node keeps track of the earliest root node that uses it, called the “successor node”
Semantically, each node runs immediately before its successor

## Slide 14: Dependency Issues
add
store r0
multiply
load r0
store r1

## Slide 15: Scheduling
List scheduler, working backwards
Minimum and maximum latency
Sometimes, we cannot schedule a node close enough to satisfy the maximum latency constraint
  “Thread” move nodes
  Not enough space for move nodes => use registers instead

## Slide 16: Scheduling
Cycle 1 |  |  | 
Cycle 2 |  |  | 
Cycle 3 |  |  | 
Cycle 4 |  |  | 
Cycle 5 |  |  | 
Cycle 6 |  |  | 

## Slide 17: Scheduling
Cycle 1 |  |  | 
Cycle 2 |  |  | 
Cycle 3 |  |  | 
Cycle 4 |  |  | 
Cycle 5 |  |  | 
Cycle 6 |  |  | 
move

## Slide 18: Pixel Processor

## Slide 19: Architecture
Vector
Barreled architecture
  100’s of threads, 128 pipeline stages
Separate thread per fragment
  explicit synchronization for derivatives and texture fetches

## Slide 20: Instructions
128 stages map to 12 “units” or “sub-pipelines” that can be enabled/disabled per instruction
Each instruction
  32-bit control word
    Instruction length
    Enabled units
  Packed bitfield of instructions for each unit, aligned to 32 bits

## Slide 21: Pipeline
Varying Fetch
Texture Fetch
Uniform/Temp Fetch
Scalar Multiply ALU
Vector Multiply ALU
Scalar Add ALU
Vector Add ALU
Complex/LUT ALU
FB Read/Temp Write
Branch

## Slide 22: Compiler
A lot easier than the GP!
High-level IR (pp_hir)
  SSA-based
  Optimizations, lowering
  Each instruction represents one pipeline stage
Low-level IR (pp_lir)
  Models the pipeline directly
  Register allocation, scheduling

## Slide 23: HIR
Lower from GLSL IR (not done yet)
Convert to SSA (hopefully not needed with GLSL IR SSA work)
Optimizations & lowering
Lower to LIR

## Slide 24: LIR
Start off with naïve translation from HIR
Peephole optimizations
  Load-store forwarding
  Replace normal registers with pipeline registers
Schedule for register pressure (registers very scarce, spilling expensive!)
Register allocation & register coalescing
Post-regalloc scheduler, try to combine instructions

## Slide 25: Mali T6xx

## Slide 26: Architecture
Somewhat similar to Pixel Processor
“Tri-pipe” Architecture
  ALU
  Load/store
  Texture
Reduced depth of each pipeline

## Slide 27: Instructions
Each instruction has 4 tag bits which store the pipeline (ALU, Load/store, texture) and size (aligned to 128 bits)
ALU instruction words are similar to before: control word, packed bitfield of instructions
Load/store words – 2 128-bit loads/stores per cycle
Texture words – texture fetches and derivatives

## Slide 28
Arithmetic
Vector Mult.
Scalar Add
Vector Add
Scalar Mult.
LUT
Output/Discard
Branch
Load/Store
Texture

## Slide 29: Future
Integration with Mesa/GLSL IR (SSA…)
Testing/optimization with real-world shaders

## Slide 30: Thank you!
Questions?