## Slide 1: What do you mean ’SDN’ on traditional routers?
Peter Van Eynde <pevaneyn@cisco.com>

## Slide 2: Who is this guy?

## Slide 3: pevaneyn@cisco.com
Physics/Lisp/ML/Networking/Security
Almost 10 years at Cisco, mostly in the Brussels TAC
  Member of security, content and SAN teams
now doing Data Science and Machine Learning
Helping with FOSDEM network also for almost 10 years

## Slide 4: The FOSDEM network

## Slide 5: Logical L2 layout
Internet
ASR1006
Info desk
K
AW
J
U
WLC
J AP’s
H
Core
ULB
VS-1
VS-2

## Slide 6: Traffic flow
Internet
ASR1006
K
AW
J
U
WLC
J AP’s
H
Core
ULB
Info desk
VS-1
VS-2

## Slide 7: Traffic flow
Internet
ASR1006
K
AW
J
U
WLC
J AP’s
H
Core
ULB
Info desk
VS-1
VS-2

## Slide 8: The hart of the network: the ASR-1006

## Slide 9: Picture here

## Slide 10: Main Features
ISSU
Non-Stop Forwarding and SSO
100 Gpbs throughput
OIR (hotplug)
Runs IOS-XE
Notes: http://www.cisco.com/c/en/us/products/routers/asr-1006-router/index.html
http://www.cisco.com/c/dam/en/us/products/collateral/routers/asr-1002-router/isocore_asr_1000_validation.pdf

## Slide 11: High level architecture
We have several levels:
RP2: Route Processor
DP with:
  ESP20: Embedded Service Processor
    FP: flow processor
    CP
  SPA Interface Procesor: SIP10: 10 Gbps/slot, doing classification, buffering
  SPA: Shared Port Adaptor
    CP
Notes: http://www.cisco.com/c/en/us/products/collateral/routers/asr-1000-series-aggregation-services-routers/white_paper_c11-452157.html

## Slide 12: RP2
Dual Intel Xeon running at 2.66GHz
16 GB of memory
80 GB HDD
Runs the routing protocols and services
This is the part you log into and where you configure the router
Newer versions can run ‘service modules’ = KVM
Notes: http://www.cisco.com/c/en/us/products/collateral/routers/asr-1000-series-aggregation-services-routers/data_sheet_c78-441072.html

## Slide 13: ESP20
CP: PowerPC based with 4G of memory
40 Mb TCAM
256 MB packet buffer
FP with 256 cores
This part actually handles the data traffic
Communicates with the RP over an internal bus, exposes an API

## Slide 14: SPA
CP: PowerPC based with 512 MB of memory
Interface cards plug into this
Handles the OIR and health checking

## Slide 15: How we monitor: 1/2 SNMP

## Slide 16
S
N
M
P

## Slide 17
Simply
Not
My
Problem

## Slide 18: What is SNMP exactly?
Notes: http://blogs.cisco.com/sp/is-snmp-here-forever-or-coauld-it-vanish-sooner-than-expected

## Slide 19: What is SNMP exactly?
Old
First release: 1988
Notes: http://blogs.cisco.com/sp/is-snmp-here-forever-or-coauld-it-vanish-sooner-than-expected

## Slide 20: SNMP: gets and traps
On the router we have an ”Agent”
Agent sends traps to management station
Ex. Interface Gi0/2/0 down
Management station gets values from Agent
Ex. Get 1.3.6.1.2.1.1.3.0

## Slide 21: SNMP: gets and traps
On the router we have an ”Agent”
Agent sends traps to management station
Ex. Interface Gi0/2/0 down
Management station gets values from Agent
Ex. Get 1.3.6.1.2.1.1.3.0
Ancient SDN: you can also SET values on the Agent

## Slide 22: What is SNMP exactly?
SNMP represents metrics in a tree, a path is an OID.
You can walk across this tree or ask for the value at a leaf.
Uses UDP to exchange information
V1 : no auth
V2: cleartext auth
V3: complex AAA
Notes: http://blogs.cisco.com/sp/is-snmp-here-forever-or-coauld-it-vanish-sooner-than-expected

## Slide 23: What do you mean?
To translate an OID into a human form you need a MIB
Actually to need several.
A MIB describes the tree using ASN.1 like syntax.

## Slide 24: MIB example
CISCO-IP-IF-CAPABILITY DEFINITIONS ::= BEGIN
… VARIATION ciiIPAddressType SYNTAX INTEGER {ipv4(1)} DESCRIPTION "Only limited set of enumerated values are supported."

## Slide 25: MIBs are messy
Downloading all standard and Cisco MIBs on Debian and enabling gives:
$ snmpget -m ALL -v2c -cpublic wlc SNMPv2-MIB::sysDescr.0 2>&1 >/dev/null | wc –l
13488
$ time snmpget -m ALL -v2c -cpublic wlc SNMPv2-MIB::sysDescr.0 2> /dev/null
RFC1213-MIB::sysDescr.0 = STRING: Cisco Controller real 0m1.183s user 0m1.124s sys 0m0.056s

## Slide 31: Example:
$ snmpwalk -Of -mALL -v2c -cpublic wlc .1.3.6.1.2.1.2 2> /dev/null | head
.iso.org.dod.internet.mgmt.mib-2.interfaces.ifNumber.0 = INTEGER: 2 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifIndex.1 = INTEGER: 1 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifIndex.2 = INTEGER: 2 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifDescr.1 = STRING: Unit: 0 Slot: .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifDescr.2 = STRING: Virtual Inter .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifType.1 = INTEGER: ethernetCsmac .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifType.2 = INTEGER: ethernetCsmac .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifMtu.1 = INTEGER: 1500 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifMtu.2 = INTEGER: 1500 .iso.org.dod.internet.mgmt.mib-2.interfaces.ifTable.ifEntry.ifSpeed.1 = Gauge32: 1000000000

## Slide 32: These counters we collect from:
ASR1006
K
AW
J
U
WLC
J AP’s
H
Core
Server
Info desk
VS-1
VS-2

## Slide 33: Problems of SNMP
UDP
Getnext/getbulk
No HA
Pull not push (expect delays)
Verbose packet format
Goes across data the wrong way
AAA in v3 is complex
Notes: http://blogs.cisco.com/sp/the-limits-of-snmp

## Slide 34: How we monitor: 2/2 NetFlow

## Slide 35: What is NetFlow?
Actually it’s
Internet Protocol Flow Information eXport
aka IPFIX
aka FnF
aka NetFlow

## Slide 36: Ok what is FnF?
With FnF you can export details about the traffic passing through an interface of the router to a ’Flow Collector’
You can filter and sample the traffic and select what details to send to which collector with a subscription model.
This is not ‘legal intercept’, so no traffic itself is captured or exported.

## Slide 37: Details like?
TCP/IP tuple (source, dest, ports)

## Slide 38: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields

## Slide 39: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields
Flow statistics (packets, bytes)

## Slide 40: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields
Flow statistics (packets, bytes)
QoS measurements

## Slide 41: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields
Flow statistics (packets, bytes)
QoS measurements
VoIP performance data: jitter, drops, etc

## Slide 42: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields
Flow statistics (packets, bytes)
QoS measurements
VoIP performance data: jitter, drops, etc
BGP AS or neighbor information

## Slide 43: Details like?
TCP/IP tuple (source, dest, ports)
TCP flags, header fields
Flow statistics (packets, bytes)
QoS measurements
VoIP performance data: jitter, drops, etc
BGP AS or neighbor information
NBAR classification and analysis

## Slide 44: NBAR?
Technically NBAR2
Deep packet protocol inspection on routers
Fed from ‘protocol packs’ describing new or changed protocols.
Used to classify traffic for QoS or FnF

## Slide 45: An example protocol
asr1k#show ip nbar protocol-id 4chan Protocol Name id type ---------------------------------------------- 4chan 763 L7 STANDARD

## Slide 46: What can we extract?
asr1k(config-flow-record)#collect application smtp ? sender SMTP Sender Mail Address server SMTP Server Name

## Slide 47: What can we extract?
asr1k(config-flow-record)#collect application http ? host Host name of Origin Server containing resource referer Address the resource request was obtained from uri List of URIs and associated hit counts url Uniform Resource Locator path user-agent Software used by agent sending the request

## Slide 48: How expensive is this?
The analysis itself is fine, the ASR’s multi-processor architecture helps
Keeping track of connections uses up a lot of TCAM resources

## Slide 49: Let’s look at this live…

## Slide 50: How is the CPU load? On the RP?
asr1k#show processes cpu sorted 5min CPU utilization for five seconds: 97%/2%; one minute: 92%; five minutes: 80% PID Runtime(ms) Invoked uSecs 5Sec 1Min 5Min TTY Process 628 5751647 293028 19628 91.57% 85.45% 72.55% 0 SNMP ENGINE 114 1161336 26654467 43 1.92% 1.68% 1.66% 0 IOSXE-RP Punt S 295 1338510 43429 30820 0.00% 1.14% 1.34% 0 Flow Exporter T 407 584401 12761 45795 0.00% 0.43% 0.59% 0 BGP Scanner 611 61701 578969 106 0.48% 0.60% 0.59% 0 IPv6 ND 9 469199 28282 16590 0.72% 0.50% 0.50% 0 Check heaps
The first split is for interface traffic processing/control plane processing time.

## Slide 51: How is the CPU load? On the CP?
asr1k#show platform software status control-processor brief
Load Average Slot Status 1-Min 5-Min 15-Min RP0 Healthy 0.79 0.72 0.64 RP1 Healthy 0.00 0.00 0.00 ESP0 Healthy 0.00 0.00 0.00 ESP1 Healthy 0.02 0.04 0.01 SIP0 Healthy 0.00 0.03 0.08 SIP1 Healthy 0.00 0.00 0.00 SIP2 Healthy 0.00 0.00 0.00

## Slide 52: How is the CPU load? On the CP? (cont)
Memory (kB) Slot Status Total Used (Pct) Free (Pct) Committed (Pct) RP0 Healthy 16342672 5032196 (31%) 11310476 (69%) 11696072 (72%) RP1 Healthy 16342672 4016600 (25%) 12326072 (75%) 11690312 (72%) ESP0 Healthy 3876564 1088140 (28%) 2788424 (72%) 921056 (24%) ESP1 Healthy 3876564 1082940 (28%) 2793624 (72%) 919192 (24%) SIP0 Healthy 471812 308096 (65%) 163716 (35%) 250396 (53%) SIP1 Healthy 471812 338612 (72%) 133200 (28%) 304712 (65%) SIP2 Healthy 471812 338488 (72%) 133324 (28%) 304712 (65%)

## Slide 53: How is the CPU load? On the CP? (cont)
CPU Utilization Slot CPU User System Nice Idle IRQ SIRQ Iowait RP0 0 7.30 1.90 0.00 90.60 0.00 0.20 0.00 1 27.60 1.50 0.00 70.60 0.00 0.30 0.00 RP1 0 2.80 2.00 0.00 95.20 0.00 0.00 0.00 1 1.59 1.79 0.00 96.40 0.00 0.09 0.09 ESP0 0 12.47 17.66 0.00 69.26 0.09 0.49 0.00 ESP1 0 12.58 15.78 0.00 71.02 0.19 0.39 0.00 SIP0 0 1.20 1.40 0.00 97.30 0.10 0.00 0.00 SIP1 0 3.09 1.39 0.00 95.40 0.09 0.00 0.00 SIP2 0 2.89 1.39 0.00 95.50 0.09 0.09 0.00

## Slide 54: How is the CPU load? On the DP?
asr1k#show platform hardware qfp active datapath utilization CPP 0: Subdev 0 5 secs 1 min 5 min 60 min Input: Priority (pps) 14 9 10 10 (bps) 9608 9232 9960 10000 Non-Priority (pps) 149265 134495 131931 129176 (bps) 1140690592 1032720912 1014169936 1031210168 Total (pps) 149279 134504 131941 129186 (bps) 1140700200 1032730144 1014179896 1031220168 Output: Priority (pps) 728 421 420 390 (bps) 652648 407728 409936 386848 Non-Priority (pps) 126557 113798 110238 106377 (bps) 913961248 810312280 789140784 788663960 Total (pps) 127285 114219 110658 106767 (bps) 914613896 810720008 789550720 789050808 Processing: Load (pct) 8 7 7 7

## Slide 55: How is the TCAM load?
asr1k#show platform hardware qfp active tcam resource-manager usage QFP TCAM Usage Information 80 Bit Region Information -------------------------- Name : Leaf Region #0 Number of cells per entry : 1 Current 80 bit entries used : 0 Current used cell entries : 0 Current free cell entries : 0

## Slide 56: How is the TCAM load? (cont)
160 Bit Region Information -------------------------- Name : Leaf Region #1 Number of cells per entry : 2 Current 160 bits entries used : 148 Current used cell entries : 296 Current free cell entries : 3800 320 Bit Region Information -------------------------- Name : Leaf Region #2 Number of cells per entry : 4 Current 320 bits entries used : 144 Current used cell entries : 576 Current free cell entries : 3520

## Slide 57: How is the TCAM load? (cont)
Total TCAM Cell Usage Information ---------------------------------- Name : TCAM #0 on CPP #0 Total number of regions : 3 Total tcam used cell entries : 872 Total tcam free cell entries : 523416 Threshold status : below critical limit

## Slide 58: How many flows?
asr1k#show flow monitor FE-FM-IPv4 statistics Cache type: Normal (Platform cache) Cache size: 1000000 Current entries: 13997 High Watermark: 18415 Flows added: 19863507 Flows aged: 19849510 - Active timeout ( 1800 secs) 7626 - Inactive timeout ( 15 secs) 19841884 Packet size distribution (4403M total packets): 1-32 64 96 128 160 192 224 256 288 320 352 384 416 .000 .133 .008 .013 .005 .025 .007 .001 .016 .000 .000 .000 .012 448 480 512 544 576 1024 1536 2048 2560 3072 3584 4096 4608 .001 .001 .000 .000 .000 .020 .748 .000 .000 .000 .000 .000 .000 Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec)-------- Flows /Sec /Flow /Pkt /Sec /Flow /FlowTCP-Telnet 326922 3.4 5 791 17.7 0.4 15.5

## Slide 59: How many flows? (cont)
asr1k#show flow monitor FE-FM-IPv4 statistics …
Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec) -------- Flows /Sec /Flow /Pkt /Sec /Flow /Flow TCP-Telnet 561022 5.4 3 689 18.8 0.4 15.5 TCP-FTP 3276 0.0 6 69 0.2 2.4 15.5 TCP-FTPD 591 0.0 1 45 0.0 0.1 15.4 TCP-WWW 1322174 12.8 74 1004 957.6 4.4 15.5 TCP-SMTP 260 0.0 2 60 0.0 2.4 15.5 TCP-X 13198 0.1 1 448 0.1 0.0 15.5 TCP-BGP 117 0.0 1 40 0.0 0.0 15.5 TCP-NNTP 753 0.0 8 230 0.0 1.1 15.5 TCP-Frag 77 0.0 21 32 0.0 13.0 15.5 TCP-other 8257760 80.3 500 1153 40196.3 4.4 15.4 UDP-DNS 7407328 72.0 1 73 78.8 0.1 15.5 UDP-NTP 171090 1.6 1 75 2.2 0.8 15.5 UDP-TFTP 154 0.0 1 40 0.0 0.0 15.4

## Slide 60: What is collected?
get for a flow: 2001:07fe:0000:0000:0000:0000:0000:0053:53 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:55318 get for a flow: 2001:07fe:0000:0000:0000:0000:0000:0053:53 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:40506 get for a flow: 2001:067c:1810:f054:0000:0000:ffff:0053:53 -17> 2001:067c:1810:f051:f913:6325:1546:bcbc:63204 get for a flow: 2001:067c:1810:f054:0000:0000:ffff:0053:53 -17> 2001:067c:1810:f051:f913:6325:1546:bcbc:63181 get for a flow: 2001:067c:1810:f051:f913:6325:1546:bcbc:62282 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:53 get for a flow: 0064:ff9b:0000:0000:0000:0000:b009:9d72:80 -6> 2001:067c:1810:f051:f913:6325:1546:bcbc:52788 get for a flow: 2001:067c:1810:f051:f913:6325:1546:bcbc:49733 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:53 get for a flow: 2001:067c:1810:f055:a45a:5f85:2900:a2ef:30124 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:53 get for a flow: 2001:067c:1810:f055:a45a:5f85:2900:a2ef:47471 -17> 2001:067c:1810:f054:0000:0000:ffff:0053:53g

## Slide 61: How we analyze this?

## Slide 62: FOS software support is … sparse
Most FnF/IPFIX collectors don’t handle the extra fields
Wrote a minimalistic perl collector to just dump the packets
Then we use awk/grep/wc/gnuplot to generate statistics

## Slide 64: Back to the future… YANG and Telemetry

## Slide 65: You people all know YANG/NETCONF right?

## Slide 66: Recap: What’s wrong with SNMP?
Verbose (externally but also internally)
Doesn’t handle HA
UDP
Pull not push
Collects data in the wrong order

## Slide 67: The solution: Telemetry
Subscription based
Efficient google Google Protocol Buffer encoding
Collect once, send to all monitoring stations
More metrics, faster

## Slide 68: Models are on github:
Notes: https://github.com/YangModels/yang/tree/master/vendor/cisco

## Slide 69: Open Device Programmability Landing Page
Notes: https://developer.cisco.com/site/odp/

## Slide 70: Yang development kit
Notes: http://cs.co/ydk-gen

## Slide 71: Interesting recent blogs posts
Notes: https://communities.cisco.com/community/developer/dna/blog/2017/01/04/next-generation-network-device-programming-part1
https://communities.cisco.com/community/developer/dna/blog/2017/01/17/next-generation-network-device-programming-part2

## Slide 72: Interesting posts from the SP world:
Notes: http://blogs.cisco.com/sp/the-limits-of-snmp
http://blogs.cisco.com/sp/boring-is-the-new-awesome

## Slide 73: Programmability on IOS-XR
Notes: https://xrdocs.github.io/

## Slide 74: Ncc: example scripts and notebooks
Notes: https://github.com/CiscoDevNet/ncc

## Slide 75: One more thing…

## Slide 76: Cisco CLI Analyzer
Notes: http://www.cisco.com/c/en/us/support/web/tools-catalog.html
https://software.cisco.com/download/type.html?mdfid=286311499&catid=null&softwareid=286312309