Lesson learned from Retro-uC and search for ideal HDL for open source silicon
3/2/2019
Staf Verhaegen
Chips4Makers

---
Retro-uC
  - Open source microcontroller with a Z80, MOS 6502 and Motorola 68000 core
  - 4 kB of on-chip RAM
  - 72 5 V digital general purpose I/O pins
  - JTAG interface for programming the device
  - Optionally bootable from external I2C flash memory
  - I/O pins that can select the enabled core during reset
  - One or more UART, I2C and PWM controllers

---
Retro-uC
Planned Product Options
Retro_uC-QFN
Retro_uC-Breadboard
Retro_uC-ProtoPlus
Retro_uC-Retrino

---
Retro-uC
Planned Product Options
Retro_uC-QFN
Retrocomputing devroom@FOSDEM 2018:
“Retro-uC – An open source microcontroller with retro
instruction sets”
Retro_uC-Breadboard
Retro_uC-ProtoPlus
Retro_uC-Retrino

---
Retro-uC

---
Retro-uC
Arduino guy:
“Costs more than Arduino and has less features”
Open source guy:
“Nice, but am not looking for an Arduino board”
Retro-computing guy:
“Where is the memory bus ?“

---
Retro-uC
Arduino guy:
“Costs more than Arduino and has less features”
Open source guy:
“Nice, but am not looking for an Arduino board”
Retro-computing guy:
“Where is the memory bus ?“
First time right

---
Overview
- Retro-uc
- First time right
- Would-be solutions
- Right direction
- I want more

---
First time right
- IMHO: the main RTL faults
  - Clock is logic signal
    event based on rising and falling edge
  - Need to know what is inferred
    if <> flip-flop or mux
  - Synthesizable versus non-synthesizable
  - Blocking versus non-blocking statement
  - FPGA vs ASIC
  - RTFLRM

---
Overview
- Retro-uc
- First time right
- Would-be solutions
- Right direction
- I want more

---
Would-be solutions
- RTL improvements
  - Verilog: -1995, -2001, -2005, SystemVerilog
    VHDL: -1987, -1993, -1900, -2002, -2008
  - New constructs
    - Signed
    - @*, process (*)
    - generate
    - Record
      interface
  - But IMO no fix of fundamental problems

---
Would-be solutions
- TL-Verilog (https://www.redwoodeda.com/)
  - Improved for defining pipelines easily:
  - But IMO no fix of fundamental problems

---
Would-be solutions
- SystemC/TLM
  - C++ class library; event driven or TLM (transaction-level modeling)
  - Seems to have similar shortcomings
  - AFAIK TLM mainly for prototyping
    needs to be manually converted to event driven code

---
Would-be solutions
- C/C++/SystemC for ESL (electronic system-level) design
  - Mainly proprietary tools now (Vivado Hlx, Catapult,...)
    would like to see more love for PandA/BAMBU
    (https://panda.dei.polimi.it/)
    should investigate GAUT (http://www.gaut.fr/)
  - IMO: mainly for compute/data path application.
    Not good fit for implementing Retro-uC but would still enlarge FOSS EDA tool portfolio.

---
Would-be solutions
- MyHDL
  - RTL with nice python syntax
    should increase productivity in RTL writing
  - Based on same event driven principles as other RTLs; by design by author

---
Overview
- Retro-uc
- First time right
- Would-be solutions
- Right direction
- I want more

---
Right direction
- Chisel SpinalHDL
  - Both based on Scala

---
Right direction
- Migen/MiSoC/nmigen
  - Hardware generation next to description
  - Currently my preference but need still development

---
Overview
- Retro-uc
- First time right
- Would-be solutions
- Right direction
- I want more

---
I want more
- Compiling and debugging on the higher level
  - Now most of the time HDL converted in RTL and need to be debugged there
    Chisel allows debugging on FIRRTL level
    migen allows to simulate/verify in python (with restrictions)
  - Need compiler and debugger on the same level as the HDL next to testbenches
    like gcc/g++/gnat/... and gdb for programming code