## Slide 1: luox: An open-source, open-access web platform implementing international standards for the quantification of light
Somang Nam, Ph.D., Jennifer A. Veitch, Ph.D., & Manuel Spitschan, Ph.D. FOSDEM Lightning talks, 2022-02-06

## Slide 2: Background: Quantities that describe light sources and exposures
Light influences human perception, physiology, and behaviour
  Vision, including colour perception and image interpretation
  Circadian, neuroendocrine and sleep physiology
International consensus documents define quantities, units, and characterizations for light sources and exposures calculated from spectral data
  CIE S 026:/E:2018 defines the quantification of light exposures for retinal photoreceptors
  CIE 015:2018 and CIE 224:2017 define parameters related to colour

## Slide 3: Background: Reporting of light quantities
No guidelines for measuring and reporting the stimulus conditions in chronobiology/sleep research studies until recently
  There are many parameters to calculate
  Calculations can seem non-trivial to beginners
Goal: develop an easy-to-use, open-access web platform for calculations related to light

## Slide 4: luox
Lightweight platform for calculations based on spectral information
  Open source (GPLv3)
  No data stored anywhere
  ES6, React, and webpack
  Formatting: Prettier, ESLint - Airbnb style guide
https://luox.app/
https://github.com/luox-app/luox

## Slide 5: luox user flow

## Slide 6: luox
Calculations follow guidance from the International Commission on Illumination (CIE)
  CIE reports and standard formula were translated into JS functions using math.js
Example: Colour Fidelity Index, Rf (CIE 224:2017)
  44 formula

## Slide 7: Demo

## Slide 8: Current challenge
Precision
  Displays floating point precision up to four decimals for all quantities
  Downloaded .csv file carries higher precision
Users demand higher precision accuracy, but JS is limited to using the IEEE 754 standard
  Temporary mitigation:
    displaying intermediate calculations for power users

## Slide 9: Status and future work
The CIE has validated luox calculations related to CIE S026:2018 and CIE 1931 (x,y) chromaticity, as a black box check.
Checks will be conducted on new code for additional CIE parameters before they are launched on the site.
Additional features may be added.
Documentation on Wellcome Open Journal: https://doi.org/10.12688/wellcomeopenres.16595.2.

## Slide 10: THANK YOU
somang.nam@nrc-cnrc.gc.ca jennifer.veitch@nrc-cnrc.gc.ca
manuel.spitschan@tum.de