## Slide 1
Marc Lichtman
Roman Ziske
https://IQEngine.org
Expanding IQEngine into a Hub for Previewing RF Signal Processing Software
Notes: primary: '#4CE091',
secondary: '#136f63',
accent: '#84cae7',
neutral: '#0f172a',
'base-100': '#05041C',
'base-content': '#f4f4f5’,
My slot is 25m and that’s NOT including another 5m for speaker transition
My GRCon talk was 25m + 1m questions

## Slide 2: What is IQEngine Currently?
preview
management
analysis
(light) processing
sharing
RF recording
… all in your browser

## Slide 3: Overview Demo
<live>
Notes: Overview demo
4m

## Slide 4: Built on Top of
An open standard for saving RF recordings
It’s a binary IQ file + a JSON file
SigMF specifies how to write the JSON
At a minimum, store
  Sample rate
  Center frequency
  Datatype of IQ
Avoid data bitrot
Notes: Keep in mind binary iq is the simplest and most natural way to save IQ to a file so any other method comes with pros/cons

## Slide 5: Built on Top of
An open standard for saving RF recordings
It’s a binary IQ file + a JSON file
SigMF specifies how to write the JSON
At a minimum, store
  Sample rate
  Center frequency
  Datatype of IQ
Avoid data bitrot
Learn more about SigMF at IQEngine.org

## Slide 6: Code
Frontend uses React, TailwindCSS
  Notable deps- CodeMirror, Pyodide, PlotLy
Backend uses Python, FastAPI
A little bit of webassembly, for fast FFTs
Docs live as .mdx markdown files and render into the live docs
  https://iqengine.org/docs

## Slide 7: Running a Server with Local Recordings
While you can always open local recordings on any IQEngine instance, “serving” recordings to users who go to the site requires storing recordings in either:
Cloud blob storage
File based storage, accessible to server running the backend
  On the server itself
  NAS, mounted to file system
  Any other option that Python open() can “see”
  Specify location in .env by setting IQENGINE_BACKEND_LOCAL_FILEPATH
<show how>
Notes: Setting up local directory of recordings
Docker command
Refresh button

## Slide 8: Plugins
RF signal processing on the backend, triggered from browser
REST-based API defined in our OpenAPI spec
  Allows for plugins to be written in any language
We have examples/templates for Python, GNU Radio, Rust
SatDump
Loïc Fejoz created a Rust-based plugin
  https://github.com/loic-fejoz/iqengine-fm-receiver-plugin

## Slide 9: Python Plugin Example
Specify custom params
run() function that takes in samples
Returns either IQ samples, annotations, image, .wav

## Slide 10: GNU Radio Plugin Example
Define Python flowgraph using zeromq’s sub_source & pub_sink
run() function has its own pub/sub for feeding in samples and getting the output
Example of a three-block flowgraph to demod FM radio:
class flowgraph(gr.top_block):
def __init__(self, samp_rate):
gr.top_block.__init__(self, "GNU Radio-based IQEngine Plugin", catch_exceptions=True)
self.zmq_sub_source = zeromq.sub_source(gr.sizeof_gr_complex, 1, 'tcp://127.0.0.1:5001', 100, False, -1)
self.zmq_pub_sink = zeromq.pub_sink(gr.sizeof_float, 1, 'tcp://127.0.0.1:5002', 100, False, -1)
self.pfb_arb_resampler = pfb.arb_resampler_ccf(500e3/samp_rate, taps=[], flt_size=32)
self.analog_wfm_rcv = analog.wfm_rcv(quad_rate=500e3, audio_decimation=10)
self.rational_resampler = filter.rational_resampler_fff(interpolation=50, decimation=48, taps=[], fractional_bw=0)
self.connect(self.zmq_sub_source, self.pfb_arb_resampler)
self.connect(self.pfb_arb_resampler, self.analog_wfm_rcv)
self.connect(self.analog_wfm_rcv, self.rational_resampler)
self.connect(self.rational_resampler, self.zmq_pub_sink)

## Slide 11: Plugins Demo
<live>
Notes: 1.5m

## Slide 12: Value of GNU Radio
Implement your RF signal processing as GNU Radio blocks
  Standard framework for implementation (in C++ or Python)
  Standard installation procedure
  Standard usage of blocks/apps, including alongside other blocks and GUIs
Sharing through CGRAN.org
With a standard way to do something comes limitations, boilerplate, streaming-style interfaces

## Slide 13: FOSS RF Functionality
FOSS Dev
Build something
Share
Demo

## Slide 14: FOSS RF Functionality: Sharing ⟷ Discovery
FOSS Dev
User
Discover
Install
Run
Evaluate
Build something
Share
Demo

## Slide 15: FOSS RF Functionality: Sharing ⟷ Discovery
FOSS Dev
Build something
Share (e.g., code on GitHub)
Demo (e.g., FOSDEM talk)

## Slide 16: FOSS RF Functionality: Sharing ⟷ Discovery
User
Discover (e.g., google topic of interest)
Install (can be a barrier for some)
Run (figure out correct params/signal)
Evaluate (e.g., on user’s SDR or recordings)

## Slide 17: Concept for Low Barrier Sharing + Discovery
Centralized and community-driven site for devs to share and users to discover
RF signal processing functions exposed as plugins
  No implementation or deployment constraints (e.g., could be GPU-based)
  Must support being triggered and results returned using Plugins API
Example RF recordings to go along with plugin
Universities, individuals, orgs can show off their expertise
All in the browser for max accessibility and convenience
FOSS Dev
User
⟷

## Slide 18: Concept for Low Barrier Sharing + Discovery
Users would be able to play around with the RF function using:
  Example recordings on IQEngine
  Their own recordings
  E.g., try lowering SNR to see how well it works
Effort on the author's side:
  Add IQEngine’s REST-based interface to their function/app, or at least make it easy to call via CLI and retrieve “results”
  Containerize so it’s easy to add to plugins server base Docker image
Multiple plugins servers connected to IQEngine.org

## Slide 19: Just a concept for now
Currently IQEngine lets you preview RF recordings and datasets
With this concept you could preview RF functions/apps/software
Current plugins system offers a starting point

## Slide 20: Limitations
Some RF functions/apps can’t be easily used with recordings
E.g., srsRAN implements the LTE and 5G radio stack, which is bidirectional with tight latency requirements

## Slide 21: Ways to Contribute
Can always use more web devs!
Other ways to contribute:
  RF recordings
  Open-source signal processing implementations via the plugins system
  Python transmitter code via the siggen tool (education-oriented)
We can also use help curating recordings hosted at IQEngine.org
Discord link at top-right of IQEngine.org
Notes: Make the RF open source ecosystem more centralized, more ways to build the community

## Slide 22: Questions?
Show your support by starring the GitHub Repo! https://github.com/iqengine/iqengine