## Slide 1: CONFEDSS
Concolic execution and the puzzling practice of peripheral emulation

## Slide 2: jeffrey@NFI:~$ whoami
Lead scientist of the exploitation team
Worked at the NFI for ~10 years
Favorite area of study is the overlap between hard- & software
Expertise in reverse engineering, exploitation, emulation and non-invasive hardware attacks

## Slide 3: luke@NFI:~$ whoami
Member of the exploitation team
Worked at the NFI for almost a year
Conducted this research as part of Master Thesis at TU Delft

## Slide 4: What does the NFI do?
Almost all forensic principles in one building:
Biological traces
Chemical and physcial traces
Digital and biometric traces
Notes: Story of the Xray machine?

## Slide 5: What do we do at the NFI?
Team exploitation, part of the device forensics team.
Extracting and decrypting evidence from digital devices
Only offline methods allowed
Evidence takes many forms, from phones and USB-sticks to crypto wallets and cars

## Slide 6: How do we do this?
Reverse engineering
Exploitation
Fuzzing
Various hardware based methods

## Slide 7: Reverse engineering – Abstraction layers
Linux Kernel
Primary bootloader (PBL)
Secondary bootloader (SBL)
Aboot
Userland
Lots of library calls, strings, symbols, well defined interfaces.
Some strings, known interfaces, maybe some known device registers.
Lots of strings, symbols, well defined interfaces and known structures.
Some known protocols, maybe some strings?

## Slide 8: Reverse engineering - examples
Example:
Library
Example:
Kernel
Example:
Aboot
Example:
SBL
Example:
PBL

## Slide 9: Normal solutions
Kernels can be emulated and debugged using QEMU or KGDB
Userspace can be debugged with normal GDB
Everything before that is signed and hard to emulate
  State is unknown
  Lots of unknown hardware is still being initialized
  Lots of memory mapped peripherals

## Slide 10: Static reversing – memory state
0x14008620
0x14003680
0x14008620
0x14008640
0x140086C0
0x1400883A
0x14008624
0x14008638
actual_function
0x1400883A

## Slide 11: Static reversing – actual memory state
?????
0x14003680
?????
?????
?????
?????
?????
?????
actual_function
?????
Notes: All these addresses depend on state setup earlier in the program, which is hard to keep track of statically.

## Slide 12: Dynamic reversing - solutions
Nothing runs before the PBL, so we can assume a zeroed out memory state
All state is setup inside the emulator
Structs and their initialization become visible and understandable
Complex logic can be single-stepped to be understood

## Slide 13: Dynamic reversing – How to emulate firmware?

## Slide 14: Emulation problems – memory map
DRAM
(uninitialized)
SRAM
Peripheral 1
Peripheral 2
Uninitialized and unpowered
Offset is known
Offset is somewhat known by reversing
Status is known, all zeroes
No logic or “asynchronous state”
Offset is usually unknown
Status is unknown
State based on unknown logic
State changes asynchrously from CPU

## Slide 15: Emulation problems - peripherals
How to emulate unknown peripherals?
Write simple hooks
How many peripherals can there be?
Start with stub hooks and implement simple logic afterwards if needed

## Slide 16: Peripheral Emulation

## Slide 17: Peripheral Emulation: Goals
Automatic
Realistic
Generic

## Slide 18: Peripheral Emulation: Solutions in Literature

## Slide 19: Intermezzo: Symbolic Execution
a = 11
b = 5
c = 0
int func(int a, int b) {
if (a == 0) {
b = 9;
} else {
a = 4;
}
c = a + b;
return c;
}
a = α
b = β
c = 0
a = 4
b = β
c = 0
a = 0
b = 9
c = 0
a = 4
b = β
c = 4 + β
a = 0
b = 9
c = 9
α == 0
α != 0
a = 4
b = 5
c = 0
a = 4
b = 5
c = 9

## Slide 20: Symbolic Peripheral Emulation
Multiple (many) states
  Some lead to successful emulation
  Others lead to infinite loops
Too many states to keep in memory
Only temporarily run symbolic execution
Concretise symbolic values “after a while”
  Concrete + Symbolic ➔ Concolic

## Slide 21: Symbolic Peripheral Emulation – Concretisation
What value?
Use different heuristics to add constraints – “Tactics”
  Nice property (i.e. “return 1 from current function”)
Use several different tactics and alternate between them

## Slide 22: Symbolic Peripheral Emulation – Tactics
DummyTactic
  Continue to next instruction
ReturnTactic(n)
  Return the value n from the current function
StepTactic(n)
  Step n states and pick a state that did not end up in a loop

## Slide 23: Peripheral Emulation – System
Analysis Tool (Ghidra)
  Provides the binary
Emulator (qiling – unicorn – QEMU)
  Uses hooks to detect Peripheral Reads / Bad States
Read Resolver (angr – z3)
  Layer between emulator and symbolic execution
  Chooses a Tactic and saves the result to History
History
  A stack (LIFO queue)
Backtracker
  Pops from History and resets Emulator

## Slide 24: Peripheral Emulation – Tactic Selection
Keep a list of usable tactics
Pick the first one
Pick next one if:
  No solutions
  10 consecutive reads from the same address
  Backtracking attempt
Backtrack if no tactics left
DummyTactic
ReturnTactic(0)
ReturnTactic(1)
StepTactic(5)

## Slide 25
int get_val() {
return *peripheral_value;
}
void init_peripheral() {
*peripheral_status |= 1;
if (*peripheral_status & 2 == 0)
while (true);
if (get_val() < 5)
panic(“Error occurred!”);
while (true) {
if (*peripheral_status & 1)
break;
}
}
Tactic
Dummy
…
0
Constraint
Value
Example

## Slide 26
int get_val() {
return *peripheral_value;
}
void init_peripheral() {
*peripheral_status |= 1;
if (*peripheral_status & 2 == 0)
while (true);
if (get_val() < 5)
panic(“Error occurred!”);
while (true) {
if (*peripheral_status & 1)
break;
}
}
Tactic
Dummy
…
0
Constraint
Value
Example
Return(0)
Return(1)
Step(5)
(x & 2 != 0) && (x != 0)
2
ERROR
ERROR

## Slide 27
int get_val() {
return *peripheral_value;
}
void init_peripheral() {
*peripheral_status |= 1;
if (*peripheral_status & 2 == 0)
while (true);
if (get_val() < 5)
panic(“Error occurred!”);
while (true) {
if (*peripheral_status & 1)
break;
}
}
Tactic
Dummy
…
0
Constraint
Value
Example
Return(0)
Return(1)
Step(5)
1
ERROR
(x == 0) && (x != 0)
(x == 1) && (x != 0)
(x >= 5) && (x != 0) && (x != 1)
5

## Slide 28
int get_val() {
return *peripheral_value;
}
void init_peripheral() {
*peripheral_status |= 1;
if (*peripheral_status & 2 == 0)
while (true);
if (get_val() < 5)
panic(“Error occurred!”);
while (true) {
if (*peripheral_status & 1)
break;
}
}
Tactic
Dummy
…
0
Constraint
Value
Example
Return(0)
Return(1)
Step(5)
ERROR
ERROR
(x & 1 != 0) && (x != 0)
1
Dummy
…
0
Dummy
…
0
…

## Slide 29: Evaluation
What combination of tactics is “best”?
  Execution time and number of peripheral reads
Accuracy: Compare against real hardware
  Run sample programs on Raspberry Pi 4B
  Compare memory, registers and instruction trace
Compare against Jetset
  State of the art – pure symbolic approach
  Run samples in Jetset
  Compare execution time and data

## Slide 30: Evaluation – Tactic Combinations
Compare different combinations of tactics
  Different paths are taken
  More tactics is not always faster
  Some combinations lead to errors
Multiple tactics are required
DummyTactic, StepTactic(5), ReturnTactic(0)

## Slide 31: Evaluation – Accuracy
Data is nearly identical
Fewer instructions
Much slower

## Slide 32: Evaluation – Comparison Jetset1 vs. CONFEDSS
Data is nearly identical
Same number of instructions
A little slower
1 2021, Johnson, E. et al.: Jetset: Targeted Firmware Rehosting for Embedded Systems in 30th USENIX Proceedings

## Slide 33
Wrongly concretised values
    Values that are used long after they have been concretised
Communication overhead

## Slide 34: Limitations
Wrongly concretised values
  Values that are used long after they have been concretised
Communication overhead

## Slide 35: Future Work
Delayed concretisation
  Keep values symbolic for longer
Connect concretised values to symbolic versions
  Tighter integration with emulator
  Implement symbolic execution-related hooks in C
  Reduce communication with emulator
Parallel evaluation of tactics

## Slide 36: Summary
Automatic, generic and realistic peripheral emulation
We built CONFEDSS, which implements this system
Available at github.com/NetherlandsForensicInstitute/CONFEDSS
Questions?