## Slide 1: Running DOS & Unix on an 8-bit Commodore
Michał Pleban

## Slide 2: Commodore PET
1977

## Slide 3: Commodore CBM-II – the PET successor
1977
1982

## Slide 4: Commodore CBM-II – the PET successor
PET |  | CBM-II
6502 @ 1 MHz | CPU | 6509 @ 2 MHz
4 – 128 kB | RAM | 128 – 1024 kB
40x25 or 80x25 text | Graphics | 80x25 text
IEE-488 disk interface | Storage | IEE-488 disk interface
 | Sound | SID
 | Expansion | Second CPU interface

## Slide 5: Multi-CPU architecture
Second CPU
Main CPU
6509
Z80, 8088, 6809, …
I/O
Shared RAM
Bus arbitrator
Message passing
Memory access

## Slide 6: Multi-CPU architecture
The second CPU can be any 8-bit CPU.
Both CPUs have access to the main memory.
Only the main CPU has access to I/O.
One CPU executes code from the main RAM, the other one runs from private memory space.
The CPUs communicate by inter-processor calls.
An IPC call alerts the second CPU to proces the call using an IRQ.
Design principles

## Slide 7: Inter-procesor calls
Second CPU → Main CPU
Second CPU (Z80) runs an operating system (CP/M)
The OS needs to read the keyboard.
Second CPU calls the main CPU to scan and read the keyboard.
Main CPU returns the key scancode.
Main CPU → Second CPU
Main CPU runs a scientific simulation.
The program requires time-consuming calculations.
Main CPU calls the second CPU (8088+8087) to perform calculations.
Second CPU stores the results in memory and exits.

## Slide 8: Implementation – the 8088 card
8088 @ 5MHz
8087 socket (not working)
CP/M-86 1.0, CP/M-86 1.1, MS-DOS 1.25

## Slide 9: Commodore MS-DOS 1.25

## Slide 10: MS-DOS today
The PC platform

## Slide 11: MS-DOS in 1982
(according to Microsoft)

## Slide 12: MS-DOS in 1982
(in reality)
>
Not PC compatible
PC compatible

## Slide 13: Can we do better?
Yes, we can™

## Slide 14: Making it PC-compatible
1
PC BIOS interrupts
2
Video memory
3
Virtual I/O devices

## Slide 15: Implementing the PC BIOS on the Commodore
Interrupt | Functions
10h | 00, 02, 03, 05, 06, 07, 09, 0A, 0E, 0F
11h | 
12h | 
13h | 00, 01, 02, 03, 04, 08, 0C, 0D, 10, 15, 16
14h | 00, 01, 02, 03
16h | 00, 01, 02
17h | 00, 01, 02
18h | 
19h | 
1Ah | 00, 01, 02, 03, 04, 05

## Slide 16: Implementing PC video memory
Video memory on the PC
RAM at B800:0000
Video memory on the Commodore
RAM at $FD000 (private area for the 6509 CPU)
Copy on timer IRQ

## Slide 17: Virtual hardware
Using a virtualization environment

## Slide 18: Virtualization environment
also known as A Piece Of Wire™
/IOREAD
/IOWRITE
/NMI
Address decoder
CPU

## Slide 19: Commodore 900
1984

## Slide 20: Commodore 900 specs
CPU | Z8001 @ 6 MHz
MMU | Z8010
Memory | 512 – 1024 kB
Graphics | 80 x 25 text 1280 x 800 bitmap
Storage | 20MB MFM drive 1 MB floppy
Operating system | Coherent 0.7.3
Connectivity | up to 6 RS-232 ports

## Slide 21: Let’s emulate!
Notes: It’s a great machine, but very rare. Because it was canceled, only a few dozen prototypes exist.
Unless you are very lucky or very rich, you can’t have one.
So how about we change that, and put a Z8000 procesor in the CBM-II to create a virtual Commodore 900!

## Slide 22: What we need:
A Z8001 CPU + Z8010 MMU ($20 on Ebay)
1 MB of RAM
16-to-8 bit memory interface
Original Commodore 900 BIOS
A Piece Of Wire™
SD card to emulate the hard disk
Coherent OS disk image.
A lot of time (priceless)

## Slide 23: The Z8001 card

## Slide 24: Thank you for your attention!
https://github.com/MichalPleban